## Slide 1: IOT and System Platform From Concepts to Code
Andy Robinson
Avid Solutions

## Slide 2: Introductions

## Slide 3: Introductions
Andy Robinson​
Information Solutions Consultant with Avid Solutions in Raleigh
2 years as Principal at Phase 2 Automation​ in Taiwan
10 years with Avid Solutions
5 years with Monsanto/Solutia in Decatur, AL and Houston, TX​
​Co-Founder of aaOpenSource
The Archestranaut​

## Slide 4: Overview

## Slide 5: Overview/One-Eyed People
I am NOT an expert
In the land of the blind
…the one eyed man is king

## Slide 6: Overview/My Definition of IOT
What would/could you do differently if the cost of the hardware and comms for your system approached $0?
Sensor
Transmitter
I/O Channel
Complex Machine
Gateway
Data Server
Visualization
Alarming
Storage
Notes: Not going to try to one up what’s been said by many people smarter than me have defined IOT in terms of the technology and the promise for hundreds of trillions of dollars in savings. Instead when I think of IOT I think about a mindset. That mindset being “what would you…”

## Slide 7: Overview/Parts and Pieces
Many Moving Pieces
Clients
Data Transmission
Servers
Storage
Visualization
Analytics
Notifications
Notes: So when you dive a little deeper you find a lot of moving parts when it comes to tx/rx of IOT data. In this talk I’m going to focus almost exclusively on the data transmission and receipt part. So… let’s get started because I’ve got about 50 slides to get through.. With demos…

## Slide 8: Overview/Data Transmission
Two Core Pieces
  Transport
    TCP – connection oriented, packets are confirmed and retransmitted if failed
    UDP - connectionless , fire and forget
  Protocol
    HTTP
    XMPP
    CoAP
    AMQP
    MQTT
Notes: Any time you send/receive data over a network you have to consider both the transport and the protocol. For transport you’ve got two primary options, TCP and UDP. The simplistic difference between the two is that TCP confirms receipt of a packet, allowing for retransmission if it doesn’t make it while UDP does not. This makes UDP a lot lighter weight and easier to wake up and send data but you have to deal with a lot of issues yourself. The next part is the protocol. And that’s what I’m about to spend a lot of time talking about. The protocol is how the two ends of the conversation know how to interpret the packets flying back and forth.

## Slide 9: Overview/Data Transmission/HTTP
Same core protocol as web page delivery
Uses a RESTful pattern with HTTP verbs (GET/POST) and specific URL’s
Client-Server with Request/Response
Notes: So first up, HTTP. This is your old school method for delivering web pages but with a new twist, a RESTFUL pattern. Without getting too far into it, RESTful patterns are a way you can use existing HTTP verbs like GET/POST, etc. and specially formulated URL’s to get data and send data to the server. But fundamentally this is a request/response pattern where every time you want data it’s a new independent transaction as well as sending data.

## Slide 10: Overview/Data Transmission/HTTP
Benefits
  Easy path through firewalls (HTTP/80, HTTPS/443)
  Out of the box transport security with SSL/TLS
  Very well known so easy to get started

## Slide 11: Overview/Data Transmission/HTTP
Drawbacks
  Huge overhead from headers 700-800 bytes1 (should be better with HTTP/2)
  RESTful patterns are inherently slow and require polling
(1) http://dev.chromium.org/spdy/spdy-whitepaper

## Slide 12: Overview/Data Transmission/XMPP
eXtensible Messaging and Presence Protocol
XML over TCP
Originally started as a chat protocol to support contact lists and presence
Ask Eliot Landrum from Stone Technologies anything
https://en.wikipedia.org/wiki/XMPP

## Slide 13: Overview/Data Transmission/XMPP
Benefits
  Open standard
  Flexible
  Very mature (originated in 1999)
https://en.wikipedia.org/wiki/XMPP

## Slide 14: Overview/Data Transmission/XMPP
Drawbacks
  No QOS inherent at the protocol layer
  Higher network overhead due to XML being text based
https://en.wikipedia.org/wiki/XMPP

## Slide 15: Overview/Data Transmission/CoAP
Constrained Object Access Protocol
UDP but similar to HTTP with RESTful functions (GET/PUT/POST/DELETE)
Asynchronous communications model
Client-Server
http://www.slideshare.net/rickgaribay/from-the-internet-of-things-to-intelligent-systems-a-developers-primer-garibay-final-34875117
http://www.realtimecommunicationsworld.com/topics/realtimecommunicationsworld/articles/408622-pros-cons-the-major-iot-communications-protocols.htm

## Slide 16: Overview/Data Transmission/CoAP
Benefits
  Ultra small header (4 bytes) leads to ultra small packet sizes
  DTLS for security
  Combined with LWM2M for robust device management
  Discovery methods built into protocol
  Great for ultra low power, ultra low bandwidth
  Datagram packet model can work over non IP transports like SMS
  IETF Standard
http://www.slideshare.net/rickgaribay/from-the-internet-of-things-to-intelligent-systems-a-developers-primer-garibay-final-34875117
http://www.realtimecommunicationsworld.com/topics/realtimecommunicationsworld/articles/408622-pros-cons-the-major-iot-communications-protocols.htm

## Slide 17: Overview/Data Transmission/CoAP
Drawbacks
  Core protocol is client-server with server initiated communications  requires inbound packets to client device  security concerns
  As single client to single server there is no built-in concept of data broadcast
http://www.slideshare.net/rickgaribay/from-the-internet-of-things-to-intelligent-systems-a-developers-primer-garibay-final-34875117
http://www.realtimecommunicationsworld.com/topics/realtimecommunicationsworld/articles/408622-pros-cons-the-major-iot-communications-protocols.htm

## Slide 18: Overview/Data Transmission/AMQP
Advanced Message Queue Protocol
Originally developed by big financial orgs for middleware messaging
Message oriented binary protocol typically over TCP
OASIS Standard
https://en.wikipedia.org/wiki/Advanced_Message_Queuing_Protocol

## Slide 19: Overview/Data Transmission/AMQP
Benefits
  Built for resiliency and scaling
  Load balancing patterns
  Messages can contain payload and metadata
  Powerful routing patterns
  Transport security based on SSL/TLS

## Slide 20: Overview/Data Transmission/AMQP
Drawbacks
  Not lightweight – built with servers and fat networks in mind (60 byte minimum packet size)
  Can be complex to implement client – thanks Paolo for SBLite

## Slide 21: Overview/Data Transmission/MQTT
Message Queue Telemetry Transport
Created by IBM and others to support oil pipeline telemetry data over slow, unreliable networks
TCP Transport
Publish-Subscribe with Broker Model
http://www.slideshare.net/rickgaribay/from-the-internet-of-things-to-intelligent-systems-a-developers-primer-garibay-final-34875117
http://www.realtimecommunicationsworld.com/topics/realtimecommunicationsworld/articles/408622-pros-cons-the-major-iot-communications-protocols.htm

## Slide 22: Overview/Data Transmission/MQTT
Benefits
  Very small header (7 bytes) leads to very small packet sizes
  TLS for transport security
  Great for low power, low bandwidth
  No incoming connection to client  much more secure
  3 levels of QOS
  OASIS Standard
http://www.slideshare.net/rickgaribay/from-the-internet-of-things-to-intelligent-systems-a-developers-primer-garibay-final-34875117
http://www.realtimecommunicationsworld.com/topics/realtimecommunicationsworld/articles/408622-pros-cons-the-major-iot-communications-protocols.htm

## Slide 23: Overview/Data Transmission/MQTT
Benefits - Small size and low overhead
https://mobilebit.wordpress.com/2013/05/03/rest-is-for-sleeping-mqtt-is-for-mobile/

## Slide 24: Overview/Data Transmission/MQTT
Drawbacks
  TCP is connection oriented so more complex to put device to sleep (MQTT-S supports UDP)
  No standard model for metadata and discoverability
  No standard method for device management
http://www.slideshare.net/rickgaribay/from-the-internet-of-things-to-intelligent-systems-a-developers-primer-garibay-final-34875117
http://www.realtimecommunicationsworld.com/topics/realtimecommunicationsworld/articles/408622-pros-cons-the-major-iot-communications-protocols.htm

## Slide 25: Overview/Data Transmission/Winner
And the best protocol is…the one that matches your requirements and capabilities
One of many comparisons
  www.slideshare.net/paolopat/mqtt-iot-protocols-comparison
Would also love to talk about DDS (ultra high performance, data-centric)
….. but let’s talk about MQTT

## Slide 26: MQTT – The Details

## Slide 27: MQTT/Details/Transport
Utilizes single, duplex, persistent TCP connection for transport
Client connects to broker and broker sends data back down the connection
Broker NEVER connects directly to client. Security Win!
Client can use SSL/TLS to connect to Broker. Security Win!
Many brokers support authentication and ACL. Security Win!
Client
Broker (Server)

## Slide 28: MQTT/Details/Communication Model
Pub/Sub with Central Broker
Conceptually similar to Mxaccess in System Platform
http://www.codeproject.com/KB/IP/PubSubUsingWCF/pubsub.png
Notes: What does pub/sub with central broker mean? What it means is you start with a central collection point called a broker. The clients that have data publish data to the broker.. Using a topic to essentially name the data point. More about topics in a minute. Then for the clients that want data they connect to same broker and subscribe to a topic or multiple topics. So when a publisher sends out an update for topic A all of the clients that are subscribed to Topic A will automatically get the updated value.

## Slide 29: MQTT/Details/Broker
Broker is meeting point for publishers and subscribers
Many different brokers available
Run locally or in the cloud

## Slide 30: MQTT/Details/Broker
Local
  mosquitto – The old man of the brokers, full featured, easy, single exe
  GnatMQ – written in C#, open source
  HiveMQ – extra features, commercial, extensible
  Mosca – node.js, open source
  Verne.MQ – written in Erlang, scalable and resilient, open source

## Slide 31: MQTT/Details/Broker
Cloud
  CloudMQTT – uses mosquitto
  Public testers – test.mosquito.org, broker.mqtt-dashboard.com, …
  Run your own on Azure

## Slide 32: MQTT/Details/Topics
Mailboxes organized into folders
“/” separates the folders
Wildcards
  Single Level  “+”
    home/+/temp
      home/1/temp
      home/2/temp
  Multi-Level  “#”
    home/#
      home/1/temp
      home/2/temp
      home/1/rh
      home/2/rh

## Slide 33: MQTT/Details/Topics vs Queues
Feature | Topics | Queues
Big Idea | Real Time | Asynchronous FIFO/Stack
Dropped Data | Can Be OK (but QOS) | Never Ok
Pub/Sub | Yes | Partial (only one client)
Applications | Sensor Data Alarms | Alarms Events Value History
“Client”
Broker
Topics
Queue
Value
Alarms
Events
HMI
Historical Values,
Alarms, Events
HMI
HMI
HMI
Publish
Subscribe
Timestamped Values
Alarms
Events

## Slide 34: MQTT – The Code

## Slide 35: MQTT/Code/Client Library
You only need a client library to pub and sub .. unless you want to run a broker too
Client libraries for almost every language
Best C# library is M2MQTT from Paolo Patierno
  Open Source
  Full Featured
  Nuget Package Available

## Slide 36: MQTT/Code/Pseudocode
Create Client
Set Options (ClientID, SSL/TLS?, QOS, Credentials)
Connect to Single Broker by Name or IP Address
…..
Subscribe to Topic(s)  Receive Callback for Subscribed Topic  Decode UTF-8 encoded binary data received
….
Publish UTF-8 encoded binary data to Topic(s)

## Slide 37: MQTT/Code/System Platform/Publish
… Declarations….
configHost = "localhost";
configclientID = Me.Tagname;
MQTTClient = new uPLibrary.Networking.M2Mqtt.MqttClient(configHost);
MQTTClient.Connect(configclientID);
if (MQTTClient.IsConnected) then
Topic = "data/" + Me.Tagname + "/value";
MQTTClient.Publish(Topic,System.Text.Encoding.UTF8.GetBytes(Me.Value));
endif;

## Slide 38: MQTT/Code/System Platform/Subscribe
Not possible due to requirement for callback registration
But you can use the AOT – been there done that.. mostly
_mqttClient.MqttMsgPublishReceived += _mqttClient_MqttMsgPublishReceived;
_mqttclient.subscribe(Topic)
…
void _mqttClient_MqttMsgPublishReceived(object sender, MqttMsgPublishEventArgs e)
{
Process new message e
}

## Slide 39: MQTT – The Demos

## Slide 40: MQTT/Demo
Demo 1 – Publishing simple data from System Platform

## Slide 41: MQTT/Demo
Demo 2 – Publishing complex data from System Platform

## Slide 42: MQTT/Demo
Demo 3 – Subscribing to Data “in” System Platform

## Slide 43: MQTT/Demo
Demo 4 – MQTT  Wonderware Historian (no System Platform)

## Slide 44: MQTT/Demo
Demo 5 – MQTT  Node-Red  ??
MQTTWarn
amqp
apns
asterisk
carbon
dbus
dnsupdate
emoncms
file
freeswitch
gss
http
instapush
irccat
linuxnotify
log
mqtt
mqttpub
mysql
mysql_dynamic
mythtv
nma
nntp
nsca
osxnotify
osxsay
pastebinpub
pipe
prowl
pushalot
pushbullet
pushover
redispub
rrdtool
slack
sqlite
smtp
syslog
twilio
twitter
xbmc
xmpp
xively
zabbix

## Slide 45: MQTT – Resources

## Slide 46: MQTT/Resources
MQTT.org
Paolo! - m2mqtt.wordpress.com/
Eclipse paho- www.eclipse.org/paho/
AMQP on Microsoft Azure - github.com/ppatierno/azuresblite
Talk to Alvaro Martinez about the new OI Server for MQTT!
aaOpenSource Github Repo github.com/aaOpenSource/aaMQTT

## Slide 47: Wrap-Up

## Slide 48: Wrap-Up/Takeaways
Just a seed
No solutions, just ideas
Take these concepts and scale up
  Consuming public MQTT data – weather? Energy prices?
  Disconnected warehouse with no VPN – real situation with current customer
We are all now composers, not luthiers

## Slide 49: Wrap-Up/Upcoming Talks
October 8 – Avid Solutions, Atlanta
  IOT – similar talk
  Basic of good security hygiene
October 20 – All Things Open – Raleigh
  Dear Open Source: Please help. Love, Manufacturing

## Slide 50: Wrap-Up/Contact
Andy Robinson
arobinson@avidsolutionsinc.com
@archestranaut
@aaOpenSource
github.com/aaopensource